## Slide 1: Scatter-and-Gather Revisited: High-Performance Side-Channel-Resistant AES on GPUs
Zhen Lin, Utkarsh Mathur, Huiyang Zhou
North Carolina State University

## Slide 2: Introduction
GPUs have been widely used for performance acceleration
  ~10x speedup for AES encryption algorithm
Side channel attacks make the crypto algorithms vulnerable
  Timing attacks
  Access-driven cache attacks
Our work: Scatter and Gather (SG) approach
  Goal: side-channel resistance & high performance
  Idea: reorganize the tables so that table lookups won’t leak key-related information

## Slide 3: Outline
Introduction
Background
Scatter-and-Gather (SG) Approach
Security Analysis
SG with Shared Memory
Evaluation
Conclusions

## Slide 4: Outline
Introduction
Background
  Memory coalescing
  Bank conflict
  AES Implementation on GPUs
  Timing attacks
  Access-driven cache attacks

## Slide 5: Memory Coalescing
Coalescing unit
0x2 Line 0
0x7 Line 1
0xB Line 2
L1 data cache
0x0
0x1
0x2
0x3
0x4
0x5
0x6
0x7
0x8
0x9
0xA
0xB
Line 0
Line 1
Line 2
Line 0, 1, 2
0x4 Line 1
Warp
tid 0
tid 1
tid 2
tid 3
Different addresses -> different # cache lines -> different access latency

## Slide 6: Bank Conflict
0x4 Bank 0
0x2 Bank 2
0x7 Bank 3
0xB Bank 3
0x0
0x4
0x8
Shared memory
Bank 0
0x1
0x5
0x9
0x2
0x6
0xA
0x3
0x7
0xB
Bank 1
Bank 2
Bank 3
Two-way
bank conflict
Warp
tid 0
tid 1
tid 2
tid 3
Different addresses -> different # bank conflicts -> different access latency

## Slide 7: AES Implementation on GPUs
Symmetric-key block-cipher algorithm, AES-128
Each thread encrypts a 128-bit block, 10 rounds
OpenSSL implementation based on table lookups
  Small tables, can fit in L1 cache or shared memory

## Slide 8: Timing Attacks on GPUs [Jiang’16]
Jiang et al., A complete key recovery timing attack on a GPU, HPCA’16
Last round:
Addr0
Addr1
Addr31
1 ~ 8 (1024/128) cache line accesses
Assume 128-byte cache line
Coalescing unit
Different access
latency
. . .
tid 0
tid 1
tid 31
Ciphertext
T-table, 1024-byte size
Input text of last round
Round key

## Slide 9: Timing Attacks on GPUs [Jiang’16]
Plaintexts | Ciphertexts | Time duration
Plaintext # 1
time1
timestart
- timestop = time1
Plaintext # 2
time2
Plaintext # 3
time3
…
…
Attacker
Server
Ciphertext # 1
Ciphertext # 2
Ciphertext # 3
…
K1 , K2 , … ,
Ki
, …
Key guesses
Correct Key
Correct Key??
Source: G. Kadam, “RCoal: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques”, HPCA’18
Notes: This should be a general timing attack description

## Slide 10: Timing Attacks on GPUs [Jiang’16]
Last round:
Inverse table lookup:
Guessed key
Table lookup address
Time (real key)
Redo table lookup
Time’ (guessed key)
High
correlation?
Table lookup timing information leaks key!

## Slide 11: Access-Driven Cache Attacks
Prime-and-Probe on CPUs
  Prime: attacker fills all cache sets
  Idle: waits for victim to access cache
  Probe: attacker monitors which cache sets were accessed by victim
  Set # => table index => key
GPU allows multiple kernels co-run on the same GPU core
  Potential threat
Attacker
Victim
L1 data cache
. . .
Data cache
Set 0
Set 1
Set x

## Slide 12: Outline
Introduction
Background
Scatter-and-Gather (SG) Approach
Security Analysis
SG with Shared Memory
Evaluation
Conclusions

## Slide 13: Scatter-and-Gather (SG) Approach
Goals
  Side channel resistance
  High performance
  Software design
Table lookups is vulnerable
Idea
  Re-organize the table so that table lookups won’t leak the key

## Slide 14: Motivation
. . .
4 bytes
4 bytes
4 bytes
256 entries (1024 bytes)
. . .
256 bytes
1024 bytes, 8 lines
1 byte
256 bytes, 2 lines
Assume 128-byte
cache line size

## Slide 15: Scatter-and-Gather (SG) Approach
32 bits
4 bits
Line 0
Line 1
1024 (256x4) bits = 128 bytes
byte 0
byte 1
byte 2
byte 3
Line 7
Line 2
Line 3
Line 4
Line 5
Line 6
1 ~ 8 lines
Constant latency!
0
1
2
255
.
.
.
0
1
2
.
.
.
255
256
entries
& 0x0000FF00
2 x 1 line

## Slide 16: For Different Cache Line Sizes
32 bits
width
0
1
2
.
.
.
255
256
entries
Cache line size | Column width | SG version
256 bytes |  | 
128 bytes |  | 
64 bytes |  | 
32 bytes |  | 
.
.
.
8 bits SG-8
4 bits SG-4
2 bits SG-2
1 bit SG-1

## Slide 17: Outline
Introduction
Background
Scatter-and-Gather (SG) Approach
Security Analysis
SG with Shared Memory
Evaluation
Conclusions

## Slide 18: Resistance to Access-Driven Cache Attacks
Original table
  Cache line # => table index
  Miss => index was accessed
Re-organized table
  Cache line # is independent on table index
  Miss won’t reveal table index
SG is resistant to access-driven cache attacks
Motivation of SG for CPUs*
[*] Blomer et al., Analysis of countermeasures against access driven cache attacks on AES, SAC’07
Line 0
Line 1
Line 7
Line 2
Line 3
Line 4
Line 5
Line 6
0
1
2
255
.
.
.
Table index
0 ~ 31
32 ~ 63
64 ~ 95
96 ~ 127
128 ~ 159
160 ~ 191
192 ~ 223
224 ~ 255
Table index

## Slide 19: Resistance to Cache Timing Attacks
Model | Architecture | L1D line size | SG-x
Tesla K40 | Kepler | 128 bytes | SG-4
GTX 980 | Maxwell | 32 bytes | SG-1
GTX 1080 | Pascal | 32 bytes | SG-1
RTX 2080 | Turing | 128 bytes | SG-4
All 16 keys can be recovered within 1000 samples! Why?
TeslaK40 GTX980 GTX1080 RTX2080
Base
SG-8
SG-4
SG-2
SG-1
16
0
0
0
16
0
0
0
16
16
16
16
16
16
16
16
# keys can be recovered in 100,000 samples
16 16 16 16

## Slide 20: A New Side Channel
// Launch kernel with 32 threads
idx = random[tid]; // Random indices (0~31)
start = clock();
dummy = input[idx] ; // Load one byte per thread
dummy ^= 0x1; // Wait for load to be finished
latency = clock() - start;
Index pattern | Latency
1 cache line access ≠ constant access latency,
vulnerable to timing attacks!
0, 1, 2, …, 31 (linear) 97 cycles
x, x, x, …, x (uniform) 97 cycles
Random_1 97 cycles
Random_2 98 cycles
Random_3 99 cycles
Random_4 100 cycles
Access the same cache line
Results on GTX 1080

## Slide 21: Outline
Introduction
Background
Scatter-and-Gather (SG) Approach
Security Analysis
SG with Shared Memory
Evaluation
Conclusions

## Slide 22: SG with Shared Memory
0x0
0x4
0x8
Shared memory
Bank 0
0x1
0x5
0x9
0x2
0x6
0xA
0x3
0x7
0xB
Bank 1
Bank 2
Bank 3
Row 0
Row 1
Row 2
1 row access == Constant latency
Confirmed with experiments!

## Slide 23: SG with Shared Memory
1024 (256x4) bits
0
1
2
255
Re-organized Table
32 bits
4 bits
0
1
2
.
.
.
255
256
entries
Original Table
Shared memory
Row 0
Row 1
Row 2
Row 3
Row 4
Row 5
Row 6
Row 7
Assume 128-byte row size

## Slide 24: Resistance to Timing Attacks
Model | Architecture | Shared mem row size | SG-x
Tesla K40 | Kepler | 256 bytes | SG-8
GTX 980 | Maxwell | 128 bytes | SG-4
GTX 1080 | Pascal | 128 bytes | SG-4
RTX 2080 | Turing | 128 bytes | SG-4
SG with shared memory is resistant to timing attacks!
TeslaK40 GTX980 GTX1080 RTX2080
Base
SG-8
SG-4
SG-2
SG-1
0
0
0
0
16
0
0
0
15
0
0
0
14
0
0
0
# keys can be recovered in 100,000 samples
16 16 16 16

## Slide 25: Resistance to Access-Driven Cache Attacks
Yes!
  Shared memory cannot be evicted

## Slide 26: Outline
Introduction
Background
Scatter-and-Gather (SG) Approach
Security Analysis
SG with Shared Memory
Evaluation
Conclusions

## Slide 27: Methodology
AES: 128-bit ECB mode
Baseline: OpenSSL ported to CUDA
4 NVIDIA GPUs:
  Tesla K40 (Kepler), GTX 980 (Maxwell), GTX 1080 (Pascal), RTX 2080 (Turing)
Open source on Github
  https://github.com/zhenlin36/scatter_gather_aes_cuda

## Slide 28: Results on GTX 1080
Baseline: OpenSSL
SG_last: SG for last round
SG_all: SG for all 10 rounds
SG_first+last: SG for first and last round
  All known attacks target first or last round
  Similar performance compared to baseline
Shared memory has higher performance
Chart: Shared memory
| 1000MB
Baseline | 290
SG-4_last | 304
SG-4_all | 100
SG-4_first+last | 301
Chart: Global memory
| 1000MB
Baseline | 135
SG-4_last | 134
SG-4_all | 29.5
SG-4_first+last | 111

## Slide 29: Overall Performance
GPU | SG_first+last throughput | % Baseline
Tesla K40 | 84 Gbps | 105%
GTX 980 | 152 Gbps | 99%
GTX 1080 | 301 Gbps | 104%
RTX 2080 | 261 Gbps | 90%
Intel Xeon CPU (E5-1607) with build in AES instructions: 27 Gbps throughput

## Slide 30: Outline
Introduction
Background
Scatter-and-Gather (SG) Approach
Security Analysis
SG with Shared Memory
Evaluation
Conclusions

## Slide 31: Conclusions
Side channel attacks make GPU vulnerable
SG approach reorganizes the tables so that the key-dependent information becomes not observable
A new side channel on GPU L1 data cache
SG with shared memory is resistant to side channels
High performance using SG_first+last

## Slide 32: Thanks & Questions

## Slide 33: Table-Based AES Implementations
Sbox AES: original implementation
  All rounds: 8-bit memory accesses
T-table AES: optimized for 32-bit processors (OpenSSL)
  First 9 rounds: 32-bit memory accesses
  Last round: 8-bit memory accesses
SG-based AES: expensive for 32-bit memory accesses
  First 9 rounds: SG-based Sbox
  Last round: SG-based T-table

## Slide 34: A New Side Channel
// Launch kernel with 32 threads
idx = random[tid]; // Random indices (0~31)
start = clock();
dummy = input[idx] ^ 0x1; // Load one byte per thread
latency = clock() - start;
Index pattern | Latency
1 cache line access ≠ constant access latency,
fixing the coalescing is not sufficient!
0, 1, 2, …, 31 (linear) 97 cycles
x, x, x, …, x (uniform) 97 cycles
Random_1 97 cycles
Random_2 98 cycles
Random_3 99 cycles
Random_4 100 cycles
4,4,8,4,4,4,4,8,4,4,4,8,4,4,4,4,8,4,4,4,4,8,4,4,4,4,4,8,4,4,4,4
0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,15,16,17,18,19,20,4,22,23,24,25,26,27,28,29,30,31
11,8,5,29,5,1,0,19,25,13,2,19,15,28,28,10,27,30,14,0,3,6,20,23,5,3,21,15,17,27,30,28
3,6,11,6,25,0,6,30,25,11,28,29,9,0,7,10,8,29,14,24,11,26,8,7,27,13,24,23,4,17,10,7
Access the same cache line
Results based on GTX 1080