## Slide 1
Nael Abu-Ghazaleh
nael@cs.ucr.edu
Is My GPU Secure? Covert and Side Channel attacks on GPUs

## Slide 2: Malware is Everywhere!
Over 350,000 malware registered every day!
Notes: The problem is that there is a lot of malware
These are what we see these days, but they are not always visible
Lets jump to what attackers really wants?

## Slide 5: Architecture support for security
What hardware
Vulnerabilities are
Exploitable by software?
What support can we
offer to improve software
Security?

## Slide 6: Graphics Processing Units
Optimize the performance of graphics and multi-media workloads
Integrated on data centers and clouds to accelerate compute
Embedded on autonomous vehicles, and other smart systems

## Slide 7: Discrete GPUs (in Desktops, Clouds, Data Centers)
General Purpose Computation:
3D Graphics
(in Desktops)

## Slide 8: Integrated GPUs: (in Desktop, Laptops, Mobile SOCs)
Graphics
Computation
Embedded GPUs in CPS systems

## Slide 9: Opportunities: Architecture & Security?
Vulnerabilities originating in architecture
  Side and covert channels
  Speculation attacks
  Fault injection
  Hardware trojans, …
Defenses rooted in architecture
  Do no harm
    Avoid vulnerabilities in architecture/HW
  Help software
    Security abstractions/mechanisms
    Computational support for expensive defenses
Attacks
Defenses

## Slide 10: Attacks based on GPU Leftover Memory
S&P
2014
TECS
2016
FC
2014
Stealing Webpages Rendered on Your Browser by Exploiting GPU Vulnerabilities (Lee et al., POSTECH)
key idea : Utilizing information leakage due to not clearing newly-allocated memory in the GPU to extract rearranged webpage textures of Chromium and Firefox web browsers
Confidentiality Issues on a GPU in a Virtualized Environment (Muarice et al.)
Key idea : leftover memory leakage in virtualized and cloud computing environments where the adversary launches a virtual machine after the victim’s virtual machine using the same GPU.
CUDA Leaks: A Detailed Hack for CUDA and a (Partial) Fix (Pietro et al.)
Key idea : Exploiting remnant state available in shared-memory, global-memory and registers.

## Slide 11: Multiprogramming on GPUs becoming widespread
Nvidia Volta Multi-Process Service (Each Volta MPS client owns its own GPU address space )
GPU Virtualization (Nvidia grid vGPU & AMD multiuser GPUs): Up to 16 client users share a GPU
Nvidia Pascal GPU supports asynchronous compute to concurrently run graphics and general purpose workloads.
Nvidia grid vGPU
Pascal asynchronous compute
AMD multiuser
Multi Process Service

## Slide 12: Motivation
GPUs often process sensitive data
Trends to improve multiprogramming on GPUs
Are side channels a threat?
  Covert channels shown
  Some side channels, but not general

## Slide 13: Outline
GPU Architecture and Programming Interfaces
Threat Model and Leakage Vectors
Side Channel Attacks:
Graphics-Graphics: Website Fingerprinting, Keystroke Timing attack
CUDA-CUDA: Neural Network model recovery
CUDA-Graphics: Website Fingerprinting
Mitigation

## Slide 14: GPU Architecture: massive paralleism

## Slide 15: GPU Programming Interfaces
Computation: CUDA and OpenCL
Graphics: OpenGL and WebGL
Programmable steps of Graphics pipeline which are executed on SMs

## Slide 16: Increasingly designed for sharing

## Slide 17: Covert Channels on GPUs – Micro’17
Malicious indirect communication of sensitive data.
Trojan
Spy
Covert Channel
Gallery App
Weather App
Why?
There is no communication channel.
The communication channel is monitored.
Covert channel is undetectable by monitoring systems on conventional communication channels.

## Slide 18: Colocation (Reverse Engineering the Scheduling)
GPU
Thread Block Scheduler
Interconnection Network
L2 Cache and Memory Channels
SM0
SM1
SMm
TB0
TB1
TBn
TB0
TB1
TBn
Kernel 1
Kernel 2
TB0
TB1
TBn
TB0
TB1
TBn
Leftover Policy
Step 1: Thread block scheduling to the SMs

## Slide 19
Warp Scheduler
Warp Scheduler
Dispatch Unit
Dispatch Unit
Register File
Shared Memory / L1 Cache
SP
SP
SP
SP
SP
SP
DP
DP
L/D
L/D
SFU
SFU
SMk
TBi
TBj
W0
W1
Wk
TB
TB
Wk-1
W0
W1
Wk
Wk-1
Step 2: Warp to warp schedulers mapping

## Slide 20: Colocation (Reverse Engineering the Scheduling)
GPU
Thread Block Scheduler
Interconnection Network
L2 Cache and Memory Channels
SM0
SM1
SMm
TB0
TB1
TBn
TB0
TB1
TBn
Kernel 1
Kernel 2
TB0
TB1
TBn
TB0
TB1
TBn
Leftover Policy
Step 1: Thread block scheduling to the SMs

## Slide 21
Warp Scheduler
Warp Scheduler
Dispatch Unit
Dispatch Unit
Register File
Shared Memory / L1 Cache
SP
SP
SP
SP
SP
SP
DP
DP
L/D
L/D
SFU
SFU
SMk
TBi
TBj
W0
W1
Wk
TB
TB
Wk-1
W0
W1
Wk
Wk-1
Step 2: Warp to warp schedulers mapping

## Slide 22: Attack Flow
Colocate Spy and Trojan
Construct the Channels
Remove Noise

## Slide 23: Cache Channel (intra-SM and inter-SM)
Extracting the cache parameters using latency plot.
(cache size, number of sets, number of ways and line size)
Communicating through one cache set.
Spy
Constant Cache set x
Constant Memory
Spy Data Array (SD)
Trojan Data Array (TD)
Trojan
Send 1
Eviction of Spy data
Cache misses
Higher Latency
Send 0
No Access!
Cache Hit
Low Latency

## Slide 24: Synchronization:
L1 Constant cache
Trojan
Spy
1
Wait (ReadytoSend)
1
Wait (ReadytoReceive)
1
0
0
1
1
0
Thread 0-5
…011001
Thread 0-5
Receive 6 bits

## Slide 25: Synchronization and Parallelization
GPU
SM 0
SM 1
SM n
…

## Slide 26: Exclusive Colocation of Spy and Trojan
Concurrency limitations on GPU hardware (leftover policy):
Shared Memory
Register
Number of Thread blocks
GPU
SM
…
TB0
TB1
TBn
TB0
TB1
TBn
Spy
Trojan
Spy
Trojan
Kmeans
Back Propagation
Heart Wall
K-Nearest Neighbor
…
No Resource Left!
Shared Memory
Register
Shared Memory
Register
Prevented interference from Rodinia Benchmark workloads on covert communication and achieved error free communication in all cases.

## Slide 27: Performance
1.7 x
3.8 x
12.9 x
Error-free bandwidth of over 4 Mbps
Constructing and Characterizing Covert Channels on GPUs [Micro 2017]

## Slide 28
Side Channel
Side channels?

## Slide 29: Finer grain microarchitectural channels
Co-location
D-cache attacks
Control flow
based attacks
CPU
GPU
Possible on different
cores / same core
Concurrent apps not possible in all scenarios (e.g. Graphics and CUDA)
Prime+Probe
Flush+Reload
…
I-cache attack
branch prediction attacks
Difficult (many active threads and small caches)
No flush instruction
SIMT computational model limits this leakage
No branch prediction

## Slide 30
Threat Model
CUDA/OpenGL Spy
on
CUDA/OpenGL Victim
CUDA Spy
on
CUDA Victim
Example Applications
GPU rendering
(Web Browsers, …)
GPU Accelerated Computations
(DNN, Encryption, …)
GPU Accelerated Computations
(DNN, Encryption, …)
Programming Interfaces
Key challenges:
How can attacker co-locate with victim
What leakage can be measured?

## Slide 31: Leakage Vectors
1
2
3
Memory allocation API : Exposes the amount of available physical memory on the GPU
GPU hardware performance counters: memory, instruction, multiprocessor, cache and texture metrics.
Timing operations: measuring the time of memory allocation events

## Slide 32: Graphics-Graphics Attack Overview
Screen
Rendering
OpenGL Spy
App

## Slide 33: Graphics-Graphics Side Channel (Co-location)
Reverse engineering the co-location of two concurrent applications:
Graphics App2
Graphics App1
CPU Code
CPU Code
GPU Code (vertex and fragment shaders)
GPU Code (vertex and fragment shaders)
CPU Code:
Read the pixel colors from framebuffer and decode the information
GPU Code (fragment shader):
Use OpenGL extensions to read ThreadID, WarpID, SMID and clock of each fragment (pixel/thread) on the GPU and encode this information in the color of each pixel.
glReadPixels(…);
SMID = float(gl_SMIDNV)/3.0;
clock = float(clock2x32ARB().y)/4294967295.0;
ThreadID = float(gl_ThreadInWarpNV)/32.0;
color = vec4(0, ThreadID ,SMID, clock);
Two graphics applications whose workloads do not exceed the GPU hardware resources can colocate concurrently.

## Slide 34: Attack 1: Website Fingerprinting
Current versions of web browsers utilize the GPU to accelerate the rendering process.
A content-related pattern (depending on the size and shape of the object) of memory allocations is performed on the GPU.
Uploading objects as Textures to the GPU
Rendering

## Slide 35: GPU memory allocation trace
OpenGL: query
“GPU_MEMORY_INFO_CURRENT_AVAILABLE_VIDMEM_NVX”
Same attack can be done by a CUDA spy using CUDA API:
“cudaMemGetInfo”

## Slide 36: Classification Results
The classification results for Memory API based website fingerprinting attack on 200 Alexa Top Websites:
  Gaussian Naive Bayes (NB)
  K-Nearest Neighbor with 3 neighbors (KNN-3)
  Random Forest with 100 estimators (RF)

## Slide 37: Attack 2: Keystroke Timing
Password bar is rendered at constant rate, when user is not typing
Password bar is rendered when user types a character
Record the timing of memory allocation events
6-character password

## Slide 38: Keystroke timing: Ground Truth vs. GPU
The probability density of the normalized measurement error with 250 key presses/timing samples
The inter-keystroke timing for 25 pairs of characters being typed

## Slide 39: CUDA-CUDA: Attack overview
CUDA Spy
App
CUDA App

## Slide 40: CUDA-CUDA Side Channel
Colocation:
Multi-Process Service (MPS) on NVIDIA GPUs allows execution of concurrent kernels from different processes on the GPU
Leakage:
Monitoring GPU Performance Counters provided by NVIDIA profiling tools
MPI Process A
MPI Process B
MPS Client Context A
MPS Client Context B
Server CUDA Context
Many to one context
MPI Service Process
Concurrent
Scheduler
Concurrent
Scheduler
Time-Sliced
Scheduler
Processors
GPU

## Slide 41: Attack 3: Neural Network Model Recovery
Victim: A CUDA-implemented back-propagation (Rodinia benchmark)
Spy: Launches several hundred consecutive CUDA kernels
Methodology:
Colocate: Reverse engineer GPU hardware schedulers to colocate on each SM
Create contention: Different threads (or warps) utilize different hardware resources in parallel to create contention
Measure: Collecting one vector of performance counter values from each spy kernel

## Slide 42: Results
The classification results for identifying the number of neurons through the side channel attack:
Input layer size varying in the range between 64 and 65536 neurons collecting 10 samples for each input size

## Slide 43: CUDA-Graphics Side Channel
Colocation (reverse engineering):
Fine-grained interleaving execution (not concurrent) of CUDA kernels and graphics operations on the GPU
Leakage:
Memory API
  From CPU, so concurrent execution
GPU Performance Counters sampling after every frame by a short CUDA kernel
Result: Classification accuracy of 93% for 200 Alexa top websites

## Slide 44: Disclosure to NVIDIA
We have reported all of our findings to NVIDIA
  Security bulletin, and CVE string
Patch: offers system administrators the option to disable access to performance counters from user processes
  Appears to be a substantial compatibility issue to take away these APIs

## Slide 45: Recap
Side channels on GPUs
  Fine grain channels impractical?
…between two concurrent applications on GPUs:
  A series of end-to-end GPU attacks on both graphics and computational stacks, as well as across them.
Mitigations based on limiting the rate and precision are effective
Future work: Multi-GPU systems; integrated GPU systems

## Slide 46
Architecture Mitigations

## Slide 47: Mitigating Contention Based Side and Covert Channel Attacks on GPUs
GPUGUARD
Classifier to detect contention
Security domains at different hierarchy levels
  maximize sharing (and performance) when it is safe

## Slide 48: Security Unit Implementation:
Tangram Security Unit
Datapath Slicing to Prevent Functional Unit Attacks
Rate Limiting Warp Scheduler to Prevent Warp Scheduling Attack
Instruction Fetch Arbitration to Prevent Instruction Cache Attack
Data Cache Re-purposing and Bypassing to Prevent Data Cache Attack.
Temporal Partitioning to Prevent Global Memory Attack
Tangram (Intra-SM Defense Framework)

## Slide 49: Results
Detection: 100% sensitivity, 8.5% false positive rate and 0% false negative rate.
8% to 23% overhead when there is an attack and zero overhead under attack
  69%-96% faster than spatial partitioning.
0.2% area overhead. 0.18% of the overall system power.
Performance impact of GPUGuard on Volta.
Attacks
Regular Apps

## Slide 50: Mitigation
Limiting the rate of the calls
Limiting the precision of returned information
Combined
(Rate limiting at 4MB granularity)

## Slide 51: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques Kadam, Zhang and Jog (College of William and Mary & Penn State University)
Defense to “A Complete Key Recovery Timing Attack on a GPU; Jiang, Fei, Kaeli, Northeastern University”
The attack uses the deterministic nature of the coalescing mechanism
Making the calculation of coalesced accesses harder for the attacker by randomizing the memory access coalescing (the size, number, and thread-elements of a sub-warp)
A trade-off between security and performance
RCOAL
HPCA-2018

## Slide 52: Memory Access Coalescing in GPUs
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x00
sid = 0
0x04
sid = 0
0x07
sid = 0
0x09
sid = 0
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
WARP
sid = subwarp id
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 1
Block Address # 2
Slide credit: Kadam et al. , HPCA 2018

## Slide 53: Memory Access Coalescing in GPUs
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
0x00
sid = 0
0x04
sid = 0
0x07
sid = 0
0x09
sid = 0
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
WARP
SUBWARP
sid = subwarp id
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 2
Slide credit: Kadam et al. , HPCA 2018

## Slide 54
RCoal: Fixed Sized Subwarp (FSS)
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
DEFAULT: number of subwarps = 1
0x00
sid = 0
0x04
sid = 0
0x07
sid = 0
0x09
sid = 0
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
FSS: number of subwarps = 2
0x00
sid = 0
0x04
sid = 0
0x07
sid = 1
0x09
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
1
Security Improves, Performance Degrades
Slide credit: Kadam et al. , HPCA 2018

## Slide 55: RCoal: Random Sized Subwarp (RSS)
Size distribution
Normal Distribution
Skewed Distribution
Mean of the distribution is same as FSS
Security and performance similar to FSS
We select RSS with Skewed Distribution
Mean of the distribution is different than FSS
Large subwarp offers better coalescing
Improved security compared to FSS
Improved performance compared to FSS


2
Slide credit: Kadam et al. , HPCA 2018

## Slide 56: Random-Threaded Subwarp (RTS)
FSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 0
0x06
sid = 1
0x07
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
FSS+RTS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 1
0x06
sid = 0
0x07
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x04
0x05
0x06
0x07
3
Slide credit: Kadam et al. , HPCA 2018

## Slide 57: RCoal: Random-Threaded Subwarp (RTS)
RSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 1
0x06
sid = 1
0x08
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
RSS+RTS: number of subwarps = 2
0x00
sid = 1
0x01
sid = 1
0x06
sid = 0
0x08
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
Slide credit: Kadam et al. , HPCA 2018

## Slide 58: Results
RCoal improves security by 24- to 961- times at a modest performance loss of 5 to 28%.
Chart: Number of Subwarp
| 1 | 2 | 4 | 8 | 16 | 32
FSS | 0.99846 | 0.99941 | 0.99935 | 0.99771 | 0.94154 | 0
FSS+RTP | 0.99846 | 0.42426 | 0.2569 | 0.080777 | 0.04366 | 0
RSS | 0.99846 | 0.2467 | 0.15489 | 0.13513 | 0.14823 | 0
RSS+RTP | 0.99846 | 0.15216 | 0.095578 | 0.10696 | 0.065268 | 0
Chart: Number of Subwarps
| 1 | 2 | 4 | 8 | 16 | 32
FSS | 1 | 1.0822 | 1.1525 | 1.2189 | 1.2788 | 1.3801
FSS+RTS | 1 | 1.082 | 1.1527 | 1.2198 | 1.2787 | 1.3801
RSS | 1 | 1.0538 | 1.104 | 1.1534 | 1.2455 | 1.3801
RSS+RTS | 1 | 1.0544 | 1.1013 | 1.1547 | 1.2455 | 1.38
Security
(Lower the better)
Execution Time
(Lower the better)
RCoal_Score
Slide credit: Kadam et al. , HPCA 2018

## Slide 59: Sugar: Secure GPU Acceleration in Web Browsers Yao, Ma, Liu, Amiri Sani and Chandramowlishwaran, University of California, Irvine
ASPLOS 2018
Current WebGL design
WebGL exposes a large Trusted Computing Base (TCB) to web apps, which are untrusted
GPU driver is buggy
Kernel driver is compromised
Vulnerabilities in GPU Process
Security checks in GPU Process is not enough, cannot protect against zero-day exploits

## Slide 60: Sugar:
Key idea: Use GPU virtualization to give an untrusted web app a separate vGPU
A dedicated virtual GPU (or vGPU) as well as all the software graphics stack (including the device driver))
Web app process is sandboxed
vGPU is isolated
Sugar’s TCB is small
Sugar’s design
Function call
Function call

## Slide 61
Future Directions
Remote WebGL-based
Attacks
Integrated GPUs
Multi-GPU systems
in HPC Clusters

## Slide 62: Integrated GPUs (Desktops, laptops and Smart Phones)
Modern SOCs: multiple CPU cores along with Integrated GPU

## Slide 63: Integrated GPUs
Memory, EDRAM and LLC are shared between CPU and GPU
Possible Threat Models:
Cross-Component Covert and Side Channels
Rowhammer on EDRAM

## Slide 64: Covert Channels
CPU-GPU share the Last-Level Cache
GPU as Trojan and CPU as Spy
Motivation: Bypassing existed mitigations on GPU and CPU for Covert Channel detection and defense
Challenge: No clock function inside OpenCL kernel =>
using Shared Virtual Memory (SVM) and Zero-Copy (Same physical memory)
  Reverse engineering the LLC on CPU side of GPU Process
  Focus on One LLC set to improve the bandwidth.

## Slide 65
time
Access Latency
Primary Result: Bandwidth : 20Kb/Sec Error rate: 0.16%
Further Bandwidth Improvement:
Transfer multiple bits over different cache set under same kernel launch
Removing kernel launch overhead

## Slide 66: Side Channel and Rowhammer
From GPU to CPU:
Challenge: building the timer.

## Slide 67: WebGL-Based Attacks
WebGL: A JavaScript API for rendering GPU-accelerated 3D and 2D graphics within web browser (based on OpenGL ES)
WebGL 1 Statistics
WebGL 2 Statistics
https://webglstats.com/

## Slide 68: Grand Pwning Unit: Accelerating Microarchitectural Attacks with the GPU Frigo, Giffrida, Bos and Razavi; Vrije Universiteit Amsterdam
S&P 2018
Using GPU as attack vector for end-to-end Rowhammer exploit from JavaScript on ARM
Using WebGL timer
After disclosure, Chrome & Firefox released partial fixes (against timers)
Attack Primitives:
DRAM accesses: Reading texture in fragment shaders
Fast cache eviction: GPU caches are small and deterministic
Contiguous memory: Performing side channel attack on DRAM row buffer to find contiguous area of physical memory
Credit: Frigo et al. S&P 2018

## Slide 69: Compute Shader in WebGL (New!)
Ability to use the general-purpose compute functionality.
Many domains: To accelerate machine learning algorithms, for image processing, to improve the rendering quality in game engines, …
Long-term: WebGPU
Short-term: WebGL 2.0 Compute (Based on OpenGL ES 3.1) (Now behind a flag) -- now accessible to developers in Google Chrome Canary by enabling flags

## Slide 70: Possible Attack:
Remote (Javascript-based) Side Channel attack: from GPU to CPU applications on Systems with Integrated GPUs.
Re-enabling all previous Javascript-based microarchitectural side channel attacks that have been mitigated, by decreasing the precision of timer, disabling shared memory or ...

## Slide 71: Multi-GPU systems:
Reverse Engineering the job scheduler and stablishing Co-location on the same cluster node
  Covert and Side Channel Attacks
  Denial of Service Attacks
Fault Injection attacks e.g. Rowhammer
Mitigations to provide HPC security

## Slide 72: Conclusions
Covert and Side channel attacks possible on GPUs
Security a first order design consideration
  We cannot just focus on performance
A lot work needed to characterize threats and understand possible defenses
New computing models-> New attacks
  Heterogeneous computing, resource disaggregation, WebGL, …